Handling Inclines

---
Problem
- Harder than it looks!
- Many robots will…
  - Loose traction
  - Topple over
Tires Slipping
Topple Over

---
Flat Ground
- Friction depends on normal force
- Traction only on driven wheels
A
B
Center of Gravity
(CG)
Normal Force
(Driven Wheels)
Normal Force
(Non-Driven Wheels)
Normal Force (Driven) = { Weight times B } over { A + B }
Normal Force (Non-Driven) = { Weight times A } over { A + B }

---
Flat Ground
- Example (A = B):
  - A = 10cm, B = 10cm, Weight = 1kg
A
B
Center of Gravity
(CG)
Normal Force
(Driven Wheels)
Normal Force
(Non-Driven Wheels)
Normal Force (Driven) = { 1kg times 10 } over { 10 + 10 } = 0.5kg
Normal Force (Non-Driven) = { 1kg times 10 } over { 10 + 10 } = 0.5kg
Equal forces on front and rear wheels

---
Flat Ground
- Example (A < B):
  - A = 5cm, B = 15cm, Weight = 1kg
A
B
Center of Gravity
(CG)
Normal Force
(Driven Wheels)
Normal Force
(Non-Driven Wheels)
Normal Force (Driven) = { 1kg times 15 } over { 5 + 15 } = 0.75kg
Normal Force (Non-Driven) = { 1kg times 5 } over { 5 + 15 } = 0.25kg
Greater force on front wheels (Good Traction)

---
Flat Ground
- Example (A > B):
  - A = 15cm, B = 5cm, Weight = 1kg
A
B
Center of Gravity
(CG)
Normal Force
(Driven Wheels)
Normal Force
(Non-Driven Wheels)
Normal Force (Driven) = { 1kg times 5 } over { 5 + 15 } = 0.25kg
Normal Force (Non-Driven) = { 1kg times 15 } over { 5 + 15 } = 0.75kg
Lesser force on front wheels (Poor Traction)

---
Summary
Keep your CG close to the driven wheels

---
Incline
- Normal force reduces (Less traction)
- Gravity pulls robot backwards
Normal
Force
Weight
Flat Ground
Weight = 1kg
Normal Force = 1kg
Backward Force = 0kg
Backwards Force
25º Incline
Weight = 1kg
Normal Force = 0.91kg
Backward Force = 0.42kg

---
Incline
- Causes CG to move away from front wheels
- Effect is more significant if CG is high
A
B
A
B
Center of Gravity
(CG)
Center of Gravity
(CG)

---
Summary
- Keep your CG close to the driven wheels
- Keep your CG low

---
Solutions
- Put the driven wheels at the back!
- Good for going UP an incline
- What happens when you’re going down?
More traction on driven wheels when going up incline!

---
Solutions
- Put the CG low and near the driven wheels
- Not too low or it won’t clear the speed bumps
Keep CG near the front driven wheels

---
Solutions
- Use tracks or 4 wheels drive
- Still need to keep CG low to prevent toppling over
- Tends to turn inaccurately
With a 4 wheels drive, both front and back wheels are driven
With tracks, the entire surface in contact with the ground is driven

---
Tracks
- Tracks have poor grip
- Rubber inserts helps, but are NOT part of core set and needs to be purchased separately.
- Use rubber bands (small ones!) to improve grip cheaply
Rubber band idea and images credit of Fernando Correia of http://www.technicbricks.com/

---
Copyright
- Created by A Posteriori LLP
- Visit http://aposteriori.com.sg/ for more tips and tutorials
- This work is licensed under a Creative Commons Attribution-ShareAlike 4.0 International License.