Scratch for Arduino
Lesson 2 – Dimmer Switch
Variables, Loops, and Light Shows*
Light Shows may be omitted due to time constraints.

---
Light Control
Today we will improve the Basic LED project by introducing dimmer effect

---
Review LED Circuit
When PIN is set to LOW (0V), there’s no voltage differential across circuit, so no current.
LED
(0V)
(PIN)
Resistor
When PIN is set to HIGH (5V), voltage differential causes current to flow and light LED.

---
Controlling Brightness
So, how can we control Brightness?
We need PWM!!!
Change Resistor
(not really programmable, but let’s revisit in the next lesson!)
Change Power
But, all of our Output pins are Digital (On/Off)

---
What is PWM?
Pulse Width Modulation (PWM)
- An efficient method to vary and control power
- Used in various electrical systems
  - Lights
  - Motors
  - Comms & others

---
Change Power
- We can On/Off or HIGH/LOW or 5V/0V
  But, what if we wanted %50 power?
- Can’t set digital output to 2.5V….
So, add Time to the equation!

---
%50 Duty Cycle
- Pick some Interval or Period (1 ms, or 1000 Hz)
- Set signal to HIGH ½ of the period (0.5 ms)
- Set signal to LOW rest of the period (0.5 ms)
- Run signal over and over...
5 V
(HIGH)
(LOW)

---
Duty Cycle

---
Duty Cycle

---
PWM Pins
- Today we’ll work with Pulse Width Modulation (PWM)
- Take note which pins support PWM
The board usually indicates which pins have PWM built-in support
In this case Pins 3,5,6,9,10,11
(see ‘~’)
All output pins are digital (LOW/HIGH), so we can only vary power using something like the PWM method

---
Let’s Get Hands-On
(The fun part…?)

---
Physical Connection
Some of the LED on the Arduino should light up after connection
This end to computer
This end to Arduino

---
Start up mBlock
- Don’t forget mLink
- Then go to https://ide.mblock.cc
- File → New
Add this one instead
Get rid of this guy

---
Connect with Arduino
- Switch to “Live” mode and click “Connect”
- Select a COM port
  You may need to [x] “Show all connectable devices”
- Click “Connect”

---
Connect with Arduino
If appears, click on it!
Followed by and “Updates”

---
Exercise 2a
Control LED Brightness

---
Review LED Circuit
When PIN is set to LOW (0V), there’s no voltage differential across circuit, so no current.
LED
(0V)
(PIN)
Resistor
(330 ohms)
When PIN is set to HIGH (5V), voltage differential causes current to flow and light LED.

---
Set PWM on LED Pin
Let’s use Keys 0-9 to set Brightness Levels.
Find the When-Key-Pressed block under Control.
For starters, let’s deal with our limits – 0 (off) and 9 (full power)
Find the Set-PWM-Output block under Pin.
Set the Pin to the one which you connected your LED Long(+) leg.
(to see the reference for this block, right click “Help”)
Test it out!

---
Challenges
Key Pressed
‘0’
‘1’
‘2’
127.5
0
255
PWM Level
For 3 levels – off, medium, high – we would use this key mapping...

---
Set PWM on LED Pin
Let’s add 1 extra level for medium power.
0 for ‘0’
LED
Should be off
127.5 for ‘5’
LED
Should be lit but dim
LED
Should be lit
brightly
255 for 9
Test it out!

---
Challenges
Key Pressed
‘0’
‘1’
‘2’
‘3’
‘4’
‘5’
‘6’
‘7’
‘8’
‘9’
0
255
PWM Level
What are the appropriate PWM levels for each Key Press ‘0’ - ‘9’?
10 power levels

---
Challenges
- Add code to control LED brightness levels using all ten digit (0-9) keys
- In your Student Handout
  - Note down the PWM levels you used for all 10 keys
  - Note down math formula to generate appropriate PWM levels for each user input (0-9)
    - Generalize for N number of inputs

---
Light Control
Back to our dimmer effect...
Can you use your program to create this effect?

---
Light Control
Sort of...
If we want a smooth dimmer effect we need to run LED through all/many PWM levels 0-255
But we don’t have enough keys or patience to press all of them, so let’s try something new!

---
Exercise 2b
Create a Dimmer Effect

---
Variables
- First, Let’s create a new Variable.
  A variable is a named piece of memory that stores information like numbers or strings.
  Its value can change, hence it is variable…
- Click on “Make a Variable”
  Under Variables menu

---
Variables
Pick a meaningful Name
Doesn’t matter much for today, but keep it “For all sprites”

---
Variables
Now we have a new variable!
These are helper function blocks associated with variables:
“set Var to 0” → “Var = 0”
“change Var by 1” → “Var = Var +1”
We will use those now.

---
Variables
Let’s play with this variable...
We can change the value in a simple program, and see the Display change
To test, keep changing this value and clicking space key to change the variable.

---
Light Control - Variable
We want to use the value in our program to change the PWM output of our LED pin
Any ideas how?

---
Light Control - Loops
What about the Dimmer Effect?
We Use Loops

---
Light Control – Loops & Variables
For instance, let’s make a simple counter:
See the variable value change:

---
Dimmer Effect
Instead of wait block, set the LED pin to the increasing PWM levels
Waits for a fraction of second..

---
Dimmer Effect
For smoother effect, change to “Upload” mode
Can only use the When Arduino Starts up event now
Need a wait now, because local set PWM doesn’t wait.
Try different speeds.
Click Upload button when ready

---
RESET to Restart
Press RESET button to restart Arduino, and rerun the uploaded program

---
Exercise 2b
Create a Dimmer Effect

---
Challenges
- After trying various durations, note the
  Wait Time that gave you the best dimmer effect in your Student Handout
  - You can also vary the PWM Level Step Size
- Extend the program to make dimmer effect run from low to high and back to low again
- Make the program run continuously like this:

---
Re-Connect with Arduino
- Switch back to “Live” mode and click “Connect”
- Select a COM port
  You may need to [x] “Show all connectable devices”
- Click “Connect”

---
Connect with Arduino
When appears, click on it!
Followed by and “Updates”

---
Extra Challenges
- Convert your variable to a Slider and use it as a graphical Variable Dimmer Switch
- Create a Graphical Dashboard to control Lights
  (on/off buttons, slider dimmers, blink buttons)
- Use a physical button to act as a Toggle Dimmer Switch (on/off)
- Use multiple LEDs to create a Light Show with blinking, dimming, and any other effects you can muster

---
Copyright
Created by A Posteriori LLP
Visit http://aposteriori.com.sg/ for more tips and tutorials
This work is licensed under a Creative Commons Attribution-ShareAlike 4.0 International License.