Scratch for Arduino
Lesson 3 – Analog Input
Potentiometers, Variables, and Etch-a-Sketch*
Etch-a-Sketch may be omitted due to safety concerns.

---
Analog Input
Today we will extend the ongoing LED project by introducing an analog input device

---
Graphical Dimmer Switch
Last week some of you may have completed the Graphical Slider control

---
Physical Dimmer Switch
Today we will be using a Potentiometer as a variable resistor, or Rheostat, to recreate the effect with a physical switch...

---
Resistors & Variable Resistors
What is electrical resistance?
a measure of the difficulty to pass an electric current through a circuit element

---
Resistors & Variable Resistors
Fixed Resistors have fixed resistance
Variable Resistors have variable resistance

---
Variable Resistors
Inside there’s a fixed resistor and a wiper that points between the minimum and maximum terminals of the resistor

---
Variable Resistors
Let’s use a multimeter to measure the minimum and maximum resistance of the wiper terminal
? ohms

---
Variable Resistors
Resistance causes voltage to drop, so the potentiometer also behaves as a Voltage Divider
0 V
5 V
0 V

---
Variable Resistors
Resistance causes voltage to drop, so the potentiometer also behaves as a Voltage Divider
0 V
5 V
5 V

---
Variable Resistors
Resistance causes voltage to drop, so the potentiometer also behaves as a Voltage Divider
0 V
5 V
2.5 V

---
Variable Resistors
Resistance causes voltage to drop, so the potentiometer also behaves as a Voltage Divider
0 V
5 V
1 V

---
Analog vs. Digital Input
Unlike the digital pins which read either 0 or 1, analog inputs can read a range of values.
0 V
5 V
Let’s find out what that input range is...
?

---
Let’s Get Hands-On
(the exciting part…?)

---
Connect to Arduino
Some of the LED on the Arduino should light up after connection
This end to computer
This end to Arduino

---
Start up mBlock
- Don’t forget mLink
- Go to https://ide.mblock.cc to start mBlock
- File → New
Get rid of this guy
Add this one instead

---
Connect with Arduino
- Switch to “Live” mode and “Connect”
- Select a COM port
  [x] “Show all connectable devices”
- If appears, click on
it followed by and
“Updates”

---
Review Breadboard
Use long strips
to create lots
of pinholes for
GND & 5v
Useful when connecting multiple devices

---
Potentiometer Circuit
GND
5 V
A0 port will read the Potentiometer wiper.
GND & 5v connected through long strips.
Leave room for the LED circuit!
5 V
+
+
-
-
-

---
Exercise 3a
Read Analog Input

---
Read Analog Input
Need to do something with the value….

---
Read Analog Input
Create a new variable.
Keep reading the Analog Input pin A0 in a loop.
Set the variable to the value.
See Monitor
on the Stage

---
Challenges
- Note in your Student Handout the min/max values for the A0 readings for the Potentiometer’s Wiper
- Write a program that:
  1) checks if Potentiometer wiper is closer to GND or closer to 5V
  2) if closer to GND
  Panda says “GND”
    else
  Panda says “5V”

---
Condition on Analog Input
The “if – then”
and “if – then - else”
conditional constructs
are very important
in programming.
They allow you to change the behavior of your program based on input or state.
Add the Panda portion &
Test it out!
Can you add conditions for 4 different outcomes?

---
Light Control
Back to our dimmer effect...
Let’s combine our LED and Potentiometer circuits to re-create this effect.

---
Challenges
Make a Physical Dimmer Switch:

---
Dimmer Switch Circuit

---
Challenges
- In your Handout, note the math required to convert
  between 0-1023 (input) and 0-255 (output)
- Then program it in mblock
  Hint: look at the map block under Data
?
0-1023
0-255

---
Exercise 3b
Mapping Input to Output

---
Variables
We should now have two variables.
One to read Potentiometer from A0.
Second to store the mapped
output PWM (0-255).

---
Dimmer Program
Read and store A0
Map and store PWM output
Output PWM to
the LED pin

---
Challenges
- Try to upload the program to the Arduino for a smoother effect.
  Just change the mode, and the start event to when Arduino starts up.
- Change the program so that the Potentiometer controls how fast the LED blinks, instead of its brightness level.

---
Exercise 3c
Move, Panda, Move!!!

---
Move, Panda, Move!
Make Potentiometer control Panda’s X-axis position.
1-D Joystick

---
Move, Panda, Move!
- Find Pand X-axis min and max (move it around)
- Map A0 to Panda’s X-limits and store in a variable (for all sprites).
- Tell Panda to set its position to that saved value.
1-D Joystick

---
Move, Panda, Move!
1-D Joystick

---
Challenges
- Make Panda point towards the new X
- Make Panda look like it’s walking by changing costumes
  - And make Panda only walk when it’s moving…
- Add a second Potentiometer to control Y.
  Like an Etch-a-Sketch!

---
Extra Challenges
Use multiple LEDs to create a Metering Effect. The bigger the reading, the more LEDs are lit.
You can start with 3 LEDs, e.g.:
if (A0 < 330) turn off everything
else if (330 < A0 < 660) turn on 1
else if (660 < A0 < 990) turn on 2
else turn on 3

---
Copyright
Created by A Posteriori LLP
Visit http://aposteriori.com.sg/ for more tips and tutorials
This work is licensed under a Creative Commons Attribution-ShareAlike 4.0 International License.