Lesson 4
(High Power)
Controlling Motors, Pumps, Deathrays, and other high power devices

---
Current Limits
- Arduino UNO max current
  - 40 mA per I/O pin
  - 200 mA total
  - 5V pin can supply 500mA (cannot control in program)
20mA
150mA
300mA
1.8A
(each motor)

---
Current Limits
- 40mA is only enough for…
  - Small LEDs
  - Small speakers
  - Sensors (...most requires very little current)

---
Transistor
- Works like a switch
  - Can control much higher current than an Arduino
  - Receives electrical signal from the Arduino to turn on or off
Works the same, but without the finger
Source
Gate
Drain

---
Transistor
Positive Voltage
Connect to Arduino Vin pin.
Can also connect to higher voltages to drive more powerful devices.
Drain
Connect to the load. Load can be a buzzer, LED, motor, etc...
Gate
Connect to Arduino I/O pin (eg. pin 11).
Transistor turns on when pin 11 is High (5V).
Transistor turns off when pin 11 is Low (0V).
Source
Connect to Gnd

---
Transistor
- Many types of transistors…
  - BJT, Darlington, MOSFET, JFET, PNP, NPN, etc…
- Model we are using: 2N7000
  - N-channel, Enhancement-mode, MOSFET
  - Max voltage 60V
  - Max current 200mA
Source
Gate
Drain

---
2N7000
- N-Channel
  - Connect transistor between Load and Ground
- Enhancement-mode
  - Supply voltage to turn on
- MOSFET
  - Gate draws very little current (...treated as zero)

---
Exercise 4
Connecting Pumps

---
Pump
- Mini-Submersible Pump
  - Red wire (positive): Connect to Vin
  - Black wire (ground): Connect to Transistor
  - Can be submerged in water
  - Cannot be reversed
  - Centrifugal type pump

---
Transistor + Pump
Here we connect gate to pin 11, but you can use any of the output pins
Source
Gate
Drain

---
Transistor + Pump
5V
- When pin 11 is low
  (0 V)
- Transistor acts like
  an opened switch
Same
Pin 11
(0V)
Gnd

---
Transistor + Pump
5V
- When pin 11 is high
  (5 V)
- Transistor acts like
  an closed switch
Same
Pin 11
(5V)
Gnd

---
Try Out
- Like an LED, we can adjust the power of the pump using PWM.
- Unlike an LED, the pump may not turn at all if the PWM power is too low
What’s the lowest power you can set and still have the pump turn?

---
Minimum Power
- Unlike an LED, a pump motor has inductance. This means that it takes a while for the current to flow.
- The pump will also need to overcome friction to start turning.
- If the PWM power is too low, it’s not enough to overcome friction.

---
Adjustable Power Program
Create a program that allows the user to set the pump power
Draw this sprite or use one of the built-in sprite
Add this script to the sprite

---
Adjustable Power Program
Add this second script to the sprite
Add this script to the Arduino device

---
Challenges
1) Add in a script for reducing power when the down key is pressed
2) Part of the code for the “Set Power”, “Up key”, and “Down Key” are the same. Convert them into a My Block.
* Using My Blocks make your code neater and easier to change.

---
My Blocks
- My Blocks (...aka Functions, Subroutines)
  - Helps breaks a complicated program into smaller parts
  - Eliminate repetition
  - When making changes, only need to change one place

---
My Blocks
3) Give it a name
2) Click “Make a Block”
1) Go to “My Blocks”

---
My Blocks
4) Fill in the “define”

---
My Blocks
5) Use the block!

---
Challenges
- Create a program that allows you to set…
  - How often to turn on the pump (eg. once every 60 seconds)
  - How long to turn on the pump each time (eg. on for 4 seconds)
  - The settings should be changeable using keyboard or mouse, but without changing the program code.

---
Bonus Challenges
- Add a potentiometer and use it to control the pump power
- Add a push button and program it to be an on-off toggle

---
Summary
- Use transistors to control high power devices
- Motors require a minimum power to start turning
- Use My Blocks to...
  - Replace repeated code
  - Break down complicated programs into smaller parts

---
Copyright
Created by A Posteriori LLP
Visit http://aposteriori.com.sg/ for more tips and tutorials
This work is licensed under a Creative Commons Attribution-ShareAlike 4.0 International License.