IR Proximity Sensor
Potentiometer
to set range
- Works by emitting IR and detecting reflection
- Range: 5-40cm (indoors)
- Use potentiometer to set sensitivity / range

---
v
Pins Connections
Sensor	Arduino
VCC	5V
GND	Gnd
OUT	Any I/O (Pin 2 to 12)
You can test sensor by plugging in power pins (GND/VCC).
There is a test LED on the sensor that lights up when triggered.

---
Sample Code
Note that the output is LOW when sensor senses proximity.
HIGH when nothing’s there...