Arduino - Basics
Programming, Electronics, and Giant Killer Robots*
* Giant Killer Robots may be omitted due to budget constraints.

---
Before we start...
- We believe in open access to knowledge
- All our slides are shared online for free
- You can print it, share it, modify it, use it to run your own courses
- This current set of slides can be found here
  (* You can also find the URL on your hand-out)

---
What is an Arduino?
Short Answer:
This is an Arduino...

---
What is an Arduino?
First we’ll need to know what is a “micro-controller”
ATmega 328
ATtiny 85

---
What is an Arduino?
Micro-controllers are...
Like a miniature computers...
- Contains processor, RAM, storage, and more
- Can be programmed like a computer
Unlike a computer...
- Provides direct electrical connection to external devices
- Can’t run Minecraft or Fortnite...
Same same...
...but different

---
What is an Arduino?
Micro-controllers can be a pain…
Require a special device to program...
AVRISP (In-System Programmer)

---
What is an Arduino?
Micro-controllers can be a pain…
Require external parts to work (eg. voltage regulator, crystal oscillator, decoupling capacitors)
Voltage Regulator (...this is the simple type)
Capacitor
Crystal Oscillator

---
What is an Arduino?
So what is an Arduino?
Combines a micro-controller with all the other components into a single device
...and many more useful components

---
What is Arduino IDE?
IDE – Integrated Development Environment
You can do all of these under one roof:
write code
build/link program
run and test it
In the olden days, these tasks were done by different software (text editor, compiler/linker, and then run it as a standalone executable...
Arduino IDE – just what you think...

---
What is Arduino IDE?
Build/Run code
Write code
Build Log
(compiler errors, comm erros)

---
What is Arduino IDE?
- Opensource
- Can communicate with all kinds of Arduino-based boards
- Available at https://ardunio.cc
  (...don’t worry, we’ll show you the link again later)

---
Arduino IDE Uses C/C++
Why learn C/C++?
- C has been around since the 70’s and still very popular.
- A lot of IoT/real-time devices are built using C. Also a lot of physical device drivers.

---
Arduino IDE → Arduino
- Code is compiled to “machine language” (something the Arduino controller can understand)
- Then uploaded to the Arduino
- And runs directly on the Arduino
Convert to Arduino code and upload
Runs on Arduino

---
Getting Started
(The fun part...)

---
Physical Connection
Some of the LED on the Arduino should light up after connection
This end to computer
This end to Arduino

---
Run Arduino IDE
1) Look for this icon and run it
2) Or go to Arduino Create (web version – will need to create Login & download Plugin)
https://create.arduino.cc/editor

---
Choose Board

---
Choose Port

---
First Program - Blink
Make the Built-In LED blink slowly, forever...
// setup function runs once when you press reset or power the board
void setup() {
  // initialize digital pin LED_BUILTIN as an output.
  pinMode(LED_BUILTIN, OUTPUT);
}
// the loop function runs over and over again forever
void loop() {
  // turn the LED on (HIGH is the voltage level)
  digitalWrite(LED_BUILTIN, HIGH);
 delay(1000); // wait for a second
  // turn the LED off by making the voltage LOW
  digitalWrite(LED_BUILTIN, LOW);
 delay(1000); // wait for a second
}
Test it out!

---
Exercise 1a
External LEDs

---
Breadboard
- Helps to make electrical connections
- Many components (eg. LEDs) can be plugged in directly
- Use dupont wires to make connections
Dupont wires
The colors doesn’t matter; they all work the same
Holes in the same row are connected
No connection across center gap
Holes by the side are connected vertically across entire board

---
LED
- Light Emitting Diode
- Longer leg connects to positive
- Shorter leg connects to ground (0V)
- Doesn’t work if connected in reverse
Short leg negative
Long leg positive

---
Connecting an LED
Important!!!
Take note of which leg of the LED is longer
In this example, the bottom leg is longer.
Long leg : Positive
Short leg : Gnd

---
Connecting an LED
Connect a wire from “GND” to the shorter LED leg.
* My shorter leg is on top.

---
Connecting an LED
Add a 330 ohm resistor.
Connect one end to the long LED leg, and the other end to an empty row.

---
Connecting an LED
Connect the other end of the resistor to the “5V” pin
The LED should light up immediately!
5V

---
Connecting an LED
This is how the electricity is flowing
From…
5V to…
Resistor to…
LED to…
GND
5V

---
Connecting an LED
Controlling the LED
To control the LED, we need to connect it to an output pin instead of 5V.
Disconnect it from 5V.
Connect it to Pin 11.
5V

---
Challenges
1) Modify your earlier program to control the external LED instead of the internal LED.
2) Program the connected LED blink continuously

---
Why the resistor?
- Arduino pins provide 5V
- Different color LEDs require different voltages
  - Red, Yellow, Infra-red:	1.8V
  - Blue, White, UV:	3.3V
  - Green:	Depends. Try 1.8V first.
- Resistor helps to reduce the voltage
- What happens when you connect 5V to a Red LED without a resistor?

---
Exercise 1b
External Inputs

---
Push Button Switch
External View
Internal View

---
Connecting a Switch
Make these connections
Resistor
Value isn’t as important as before. Recommend to pick 1000 ohm, but most other values will do as well.
Push button switch
Connects the adjacent pins. Only need to use one side...
Connected to 5V

---
Connecting a Switch
- When switch is open…
- Pin 11 is connected
  to 0V via the resistor
- Pin 11 not connected
  to 5V
5V
To Arduino
Pin 11
What is the voltage?
Voltage of pin 11
= 0 V
= False
= Low

---
Connecting a Switch
- When switch is closed…
- Pin 11 is connected
  to 0V via the resistor
- Pin 11 is connected
  to 5V directly
5V
To Arduino
Pin 11
What is the voltage?
Voltage of pin 11
= 5 V
= True
= High

---
Connecting a Switch
- This resistor is call a pull-down resistor, because it pulls the voltage down to 0V when the switch is open
- We can also connect the resistor to 5V and the switch to Gnd. This is call a pull-up resistor.

---
Connecting a Switch
- Can we connect the switch to Gnd without a resistor?
  - NO! Without the resistor,
    we will have a short
    circuit when the switch
    is pressed
When switch is pressed
5V
Positive connected directly to negative.
Short circuit!

---
Connecting a Switch
Connected to 5V

---
Button Sample Code
// constants won't change. They're used here to set pin numbers:
const int buttonPin = 11; // the number of the pushbutton pin (see connection above)
const int ledPin = 13; // the number of the LED pin
// variables will change:
int buttonState = 0; // variable for reading the pushbutton status
void setup() {
  // initialize the LED pin as an output:
  pinMode(ledPin, OUTPUT);
  // initialize the pushbutton pin as an input:
  pinMode(buttonPin, INPUT);
}
void loop() {
  // read the state of the pushbutton value:
  buttonState = digitalRead(buttonPin);
  // check if the pushbutton is pressed. If it is, the buttonState is HIGH:
  if (buttonState == HIGH) {
    // turn LED on:
    digitalWrite(ledPin, HIGH);
  } else {
    // turn LED off:
    digitalWrite(ledPin, LOW);
  }
}

---
Challenges
1) Make an LED blink rapidly for 2 seconds when the button is pressed
2) Make an LED toggle between on and off when the button is pressed

---
Copyright
Created by A Posteriori LLP
Visit http://aposteriori.com.sg/ for more tips and tutorials
This work is licensed under a Creative Commons Attribution-ShareAlike 4.0 International License.