Lesson 2 – PWM & Dimming Effect
Variables, Loops, and Light Shows*
Light Shows may be omitted due to time constraints.

---
Light Control
In this lesson we will improve the Basic LED project by introducing dimmer effect

---
Digital vs. Analog
Digital
0 or 1	LOW or HIGH	0v or 5v
Analog
Range of integers or real numbers

---
Digital vs. Analog
POWER
PINS
DIGITAL
INPUTS &
OUTPUTS
ANALOG
INPUTS

---
Controlling Brightness
So, how can we control Brightness?
We need PWM!!!
Change Resistor
(not really programmable, but let’s revisit in another lesson!)
Change Power
But, all of our Output pins are Digital (On/Off)

---
What is PWM?
Pulse Width Modulation (PWM)
- An efficient method to vary and control power
- Used in various electrical systems
  - Lights
  - Motors
  - Comms & others

---
Change Power
- We can On/Off or HIGH/LOW or 5V/0V
  But, what if we wanted %50 power?
- Can’t set digital output to 2.5V….
So, add Time to the equation!

---
%50 Duty Cycle
- Pick some Interval or Period (e.g. 1 ms, or 1000 Hz)
- Set signal to HIGH ½ of the period (0.5 ms)
- Set signal to LOW rest of the period (0.5 ms)
- Run signal over and over...
5 V
(HIGH)
(LOW)

---
Duty Cycle

---
Duty Cycle

---
PWM Pins
- Today we’ll work with Pulse Width Modulation (PWM)
- Take note which pins support PWM
The board usually indicates which pins have PWM built-in support
In this case Pins 3,5,6,9,10,11
(see ‘~’)
All output pins are digital (LOW/HIGH), so we can only vary power using something like the PWM method

---
Let’s Get Hands-On
(The fun part…?)

---
Review LED Circuit
When PIN is set to LOW (0V), there’s no voltage differential across circuit, so no current.
LED
(0V)
(PIN)
Resistor
When PIN is set to HIGH (5V), voltage differential causes current to flow and light LED.

---
Physical Connection
Some of the LED on the Arduino should light up after connection
This end to computer
This end to Arduino

---
Exercise 1
Control LED Brightness

---
Review LED Circuit
When PIN is set to LOW (0V), there’s no voltage differential across circuit, so no current.
LED
(0V)
(PIN)
Resistor
(330 ohms)
When PIN is set to HIGH (5V), voltage differential causes current to flow and light LED.

---
Vary PWM on LED Pin
int ledPin = 11; // LED connected to digital pin 11
void setup() {
  pinMode(ledPin, OUTPUT);
}
void loop() {
  // let's test different values
  analogWrite(ledPin, 255); // %100 duty cycle
  delay(1000); // sleep to get a chance to see the effect
  analogWrite(ledPin, 190); // %75
  delay(1000);
  analogWrite(ledPin, 127); // %50
  delay(1000);
  analogWrite(ledPin, 63); // %25
  delay(1000);
}
Test it out!

---
Exercise 2
Create a Dimmer Effect

---
Light Control
Back to our dimmer effect...
Can you use your program to create this effect?

---
Challenges
- Hint: Use Loops (for, while, etc)
- Try different PWM Step Sizes
  - You can also vary Delay/Sleep Times
- Extend the program to make dimmer effect run from low to high and back to low again

---
For-Loop PWM Dimmer
int ledPin = 11; // LED connected to digital pin 11
void setup() {
  pinMode(ledPin, OUTPUT);
}
void loop() {
  // fade in from min to max values in increments of 5:
  for (int fadeValue = 0 ; fadeValue <= 255; fadeValue += 5) {
    analogWrite(ledPin, fadeValue);
    delay(30); // wait 30ms to see the dimming effect
  }
  // Then fade out...
  for (int fadeValue = 255 ; fadeValue >= 0; fadeValue -= 5) {
    analogWrite(ledPin, fadeValue);
    delay(30);
  }
}
Test it out!

---
Extra Challenges
- Change the For Loop to a While Loop
- Use a physical button to act as a Toggle Dimmer Switch (on/off)
- Use multiple LEDs to create a Light Show with blinking, dimming, and any other effects you can muster

---
RESET to Restart
Press RESET button to restart Arduino, and rerun the uploaded program

---
Copyright
Created by A Posteriori LLP
Visit http://aposteriori.com.sg/ for more tips and tutorials
This work is licensed under a Creative Commons Attribution-ShareAlike 4.0 International License.