Lesson 3
(High Power)
Controlling Motors, Pumps, Deathrays*, and other high power devices
* No, not for reals...

---
Current Limits
- Arduino UNO max current
  - 40 mA per I/O pin
  - 200 mA total
  - 5V pin can supply 500mA
    (but, cannot be controlled in program)
20mA
150mA
300mA
1.8A
(each motor)

---
Current Limits
- 20mA is only enough for…
  - Small LEDs
  - Small speakers
  - Sensors (...most requires very little current)

---
Transistor
- Works like a switch
  - Can control higher current than an Arduino I/O pin
  - Arduino I/O pin can be used to turn on or off
Works the same, but without the finger
Source
Gate
Drain

---
Transistor
Positive Voltage
Connect to Arduino 5V pin.
Can also connect to higher voltages to drive more powerful devices.
Drain
Connect to the load. Load can be a buzzer, LED, motor, etc...
Gate
Connect to Arduino I/O pin (eg. pin 11).
Transistor turns on when pin 11 is High (5V).
Transistor turns off when pin 11 is Low (0V).
Source
Connect to Gnd

---
Transistor
- Many types of transistors…
  - BJT, Darlington, MOSFET, JFET, PNP, NPN, etc…
- Model we are using: 2N7000
  - N-channel, Enhancement-mode, MOSFET
  - Max voltage 60V
  - Max current 200mA
Source
Gate
Drain

---
2N7000
- N-Channel
  - Connect transistor between Load and Ground
- Enhancement-mode
  - Supply voltage to turn on
- MOSFET
  - Gate draws very little current (...treated as zero)

---
Exercise 1
Connecting Pumps

---
Pump
- Mini-Submersible Pump
  - Red wire (positive): Connect to 5V
  - Black wire (ground): Connect to Transistor
  - Can be submerged in water
  - Cannot be reversed
  - Centrifugal type pump

---
Transistor + Pump
Here we connect gate to pin 11, but you can use any of the output pins
Source
Gate
Drain

---
Transistor + Pump
5V
- When pin 11 is low
  (0 V)
- Transistor acts like
  an opened switch
Same
Pin 11
(0V)
Gnd

---
Transistor + Pump
5V
- When pin 11 is high
  (5 V)
- Transistor acts like
  an closed switch
Same
Pin 11
(5V)
Gnd

---
Exercise 2
Controlling Pumps

---
Try It Out
- Like an LED, we can adjust the power of the pump using PWM.
- Unlike an LED, the pump may not turn at all if the PWM power is too low
What’s the lowest power you can set and still have the pump turn?

---
Minimum Power
- Unlike an LED, a pump motor has inductance. This means that it takes a while for the current to flow.
- The pump will also need to overcome friction to start turning.
- If the PWM power is too low, it’s not enough to overcome friction.

---
Up / Down Power
Use 2 buttons as Up/Down power inputs – when Up is pressed, the power increases (pump pumps faster), and when Down is pressed the power decreases…
You can use the Serial Monitor and Serial Arduino class to see the power being used in the program.

---
UpDown Buttons
const int upPin = 2; // the Up pushbutton pin
const int pumpPin = 11; // the pump pin
int power = 0; // variable for remembering & setting power level
void setup() {
  pinMode(pumpPin, OUTPUT);
  pinMode(upPin, INPUT);
  Serial.begin(9600); // Create a Serial
  Serial.println("Power Settings");
}
void loop() {
  int upState = digitalRead(upPin);
  if (upState == HIGH) {
    power += 10;
    Serial.println(power);
    delay(500); // button freeze, to avoid undesired behavior (test without!)
  }
  analogWrite(pumpPin, power);
}

---
Serial Monitor
Make sure to match the Baud rate here with the one in your program: Serial.begin(9600);

---
Challenges
Hand Sanitizer with Button
- Create a program and circuit that…
  - Has a button to initiate pump squirts
  - Creates a “Off Time” to prevent over-squirting…
    Can use an LED to indicate when the program is ready to squirt again...

---
Functions
Use Functions to Simplify Code:
- Reduce code repetition / redundancy
- Avoid long, hard-to-decipher programs - everything put into one big Loop() function
- Create code bits that are easy to understand and follow
- Modularize the code for quick changes

---
Functions
Simplify code by using functions, like “void squirt(int power, int time)”, which makes the pump turn on with a certain power and time to effect a squirt.
int pumpPin = 11; // Pump transistor connected to digital pin 11
void setup() {
  pinMode(pumpPin, OUTPUT);
}
void squirt(int power, int time) {
  // Turn on pump with indicated power, for indicated duration, and then shut it
  analogWrite(pumpPin, power);
  delay(time);
  analogWrite(pumpPin, 0);
}
void loop() {
  // Use a button to initiate squirts
  squirt(100, 500);
  delay(5000);
}

---
Summary
- Use transistors to control high power devices
- Motors require a minimum power to start
- Use Functions to...
  - Replace repeated code
  - Break down complicated programs into smaller parts

---
Copyright
Created by A Posteriori LLP
Visit http://aposteriori.com.sg/ for more tips and tutorials
This work is licensed under a Creative Commons Attribution-ShareAlike 4.0 International License.